Timing Constraints and Pipelining
Austin FPGA Meetup
 August 9th, 2021
Michelle Guardabascio

---
It’s Time!
- Previous beginner labs: “Don’t worry about timing. We’ll deal with that later”.
- It’s later!
- We’re going to learn about timing constraints, timing failures, and how to fix them with pipelines!
- We finally get to see timing warnings like this!

---
Objectives
1. Review example project design and code
2. Understand basics of pipelining
3. How to create a timing constraints file using Quartus; observe that timing fails
4. Understand Quartus timing report information
5. Implement pipelining in our designs to resolve timing failures; observe that timing passes

---
Software/Hardware Used
- DE1-SoC Evaluation Board
- DE1-SoC User Manual
- Quartus Tool & Quartus Cyclone V Support File
- Terasic Board Device Drivers

---
DE1-SoC
- Available from Terasic
- https://www.terasic.com.tw/cgi-bin/page/archive.pl?Language=English&No=836
- $249 ($175 Academic)
- 64-bit OS and Quartus II 64-bit are required to compile projects

---
Project Modules Overview
- Example project for pipeline lesson:
    - Reads values from device
    - Apply FIR filter to data we read
    - Write filtered data to memory
- Modules for our example project:
    - SPI – from previous labs
    - A2D – from previous labs
    - Inferred memory – new to this lab
    - FIR Filter – new to this lab

---
Project Module Hierarchy

---
Project Module Data Flow

---
Inferred Memory Module
- Synchronous; single clock
- Dual port RAM; Can read and write and the same time
- I/O

---
Inferred Memory Port Signals
module single_clock_dual_ram
#( // port parameters
parameter int ADDRESS_LEN = 8,
parameter int RAM_WIDTH = 8,
parameter int RAM_DEPTH = (2 ** ( ADDRESS_LEN )) // Do not override this
)
( // port signals
input logic clock,
// no resets on memory
input logic [ADDRESS_LEN - 1:0] read_address,
output logic [RAM_WIDTH - 1:0] data_out,
input logic write_enable,
input logic [ADDRESS_LEN - 1:0] write_address,
input logic [RAM_WIDTH - 1:0] data_in
);

---
Inferred Memory Implementation
// Implementation
always_comb
begin
if ( write_enable == 1'b1 )
begin
mem_next [ write_address ] = data_in;
end
data_out_next = mem [ read_address];
end
// Register the output of combinational logic
always @ (posedge clock)
begin
mem <= mem_next;
data_out <= data_out_next;
end

---
FIR Filter Module
- We will use pipelining to implement this module
- This module will fail to meet the timing requirements when we build the project
- We will learn how to do additional pipelining after the timing failure so that the project will meet timing requirements
- Background items to discuss before we discuss the FIR Filter Module:
    - Introduction to pipelines
    - Introduction to the FIR Filter.
- Then we’ll look at the FIR Filter Module’s code

---
What Is a Pipeline?
- A technique to improve throughput by dividing the project’s work up into individual tasks
- This works something like an assembly line
- An individual item will not be completed faster – maybe even a little slower
- Overall, the system will complete more work for a given amount of time

---
Pipeline: Laundry Example (1 of 2)
- There are 3 steps in the process
    - (W) Washing – 35 minutes
    - (D) Drying – 45 minutes
    - (F) Folding – 20 minutes
- The washer accommodates 20 items of clothing per load
- We have 200 items to wash
- If we do laundry sequentially; no pipelining, it looks like this: W D F W D F ...
    - 10 loads
    - Each has a latency of 100 minutes
    - 1000 minutes to wash all the laundry
    - We process about 12 items of clothing per hour

---
Pipeline: Laundry Example (2 of 2)
- While washing, dryer idle; while drying, washer idle; while folding, both washer and dryer are idle.
- So, let’s operate in parallel
- The drying phase is the longest at 45 minutes. With 10 loads, that’s 450 minutes.
- Add time for the first wash, 35 minutes, and the last fold, 20 minutes, the total time is 505 minutes.
- We process about 23.76 items per hour.
- This is about twice as fast as our non-pipelined example.
    - Note that the time taken to launder one shirt remains the same.
    - The system throughput is improved.
  This example taken from: http://hpca23.cse.tamu.edu/taco/utsa-www/cs5513-fall07/lecture3.html

---
FIR Filter Introduction
- Finite Impulse Response (FIR) filters use only delayed versions of the input signal to filter the input to the output
- Finite: no feedback (IIR have feedback)
- A basic and common Digital Signal Processing (DSP) filter
- Removes noise
- Pro: simple to implement
- Con: require many math calculations
- A tap is a coefficient/delay pair
- Delay line is the implementation of the delay part of the filter algorithm

---
FIR Filter – How We Will Use It
- 16 taps
- Low pass: low frequencies pass through the filter and high frequencies are attenuated; this is how noise is removed
- The coefficients can be obtained from MATLAB or similar tools.

---
FIR Module I/O

---
FIR Filter Module Port Signals

---
FIR Module Steps
- Like the laundry example, our FIR filter has 3 steps:
    - Move data through the delay line
    - Multiply the values by their per-calculated coefficient
    - Sum the products to create the filtered_output
- The coefficients can be computed with MATLAB or one of several online FIR Filter tools

---
FIR Module FPGA Implementation

---
FIR Module –The 3 Steps Verilog

---
Pipeline – The FIR Filter Module
We anticipate that this module is the one that’s going to cause us to not meet our timing requirements.
Why?
Because it’s does many math calculations.
There are 16 32-bit integer additions.
There are 16 16-bit integer multiplications

---
Adding Timing Constraints
- We’re done with coding
- We’re going to add our timing constraints to the Quartus tool
- We need to add timing constraints for
    - Each clock
    - Each I/O path (ports of the top level module)
- We have one clock:
    - system clock
    - it’s a 50MHz clock that we are using on our evaluation board
    - we’re going to lie and say it’s 200 MHz (a medium FPGA speed) so that we will be able to demonstrate timing constraints failure and resolution
    - Timing will actually pass at 50 MHz
- Each I/O path – these are the ports of the top level module
    - We have the SPI signals; these are implemented in I/O flip-flops which don’t require timing restraints because these are implemented with timing constraints for us in the I/O flip-flop
        - Because IO flops have dedicated, fixed routing, so timing is ensured/guaranted by construction/design
        - Therefore timing failures on IO flops are impossible
        - You would specify timing constraints for an IO buffer if a clock buffer drives an IO pin
            - Often done in high speed protocols. One example is PCI express
            - This is the exception; you’re usually adding timing constraints for clocks
    - We have the reset signal; this is also implemented in an I/O flip-flop.
    - Finally we have the filtered value that we wrote to memory. For now, it is a dummy signal. It will remain there until we read the memory in an upcoming lab.
As such, the only signal that we will add a timing constraint for is the system_clock.

---
Add Timing Constraints to Project
- We’re going to use the TimeQuest Timing Analyzer Wizard
- In Quartus, select Tools> TimeQuest Timing Analyzer
- The TimeQuest Timing Analyzer will open in a separate window. In it, select Tools > TimeQuest Timing Analyzer Wizard ...
- The Wizard will open in a new window

---
TimeQuest Analyzer Wizard

---
TimeQuest Analyzer Wizard Data
- We are specifying a 200 MHz system_clock:
  - 5 ns Period
  - 0 Rising
  - 2.5 Falling
- Note that we enter “system_clock” in both the Clock_Name field as well as the “Input_Pin” field and we do not enter the actual input pin.
- The input pin for the system_clock is specified in the .qsf file

---
TimeQuest Analyzer Wizard Finish
- Select “Next” four more times
- Accept the default name for the timing constraints .sdc file
- Select “Finish”

---
Timing Constraints (.sdc) file

---
Build Project – Timing Fails
- Build project and observe that there are warnings about timing not meeting specifications.
- This is because we created a timing constraints (.sdc) file and the timing requirements specified are not met.
- Let’s look at the timing report information to see what the problem is and what we should do about it.

---
Access Timing Reports (1 of 4)
- In Quartus, select Tools> TimeQuest Timing Analyzer
- The TimeQuest Timing Analyzer will open in a separate window.
- Double-click the “Create Timing Netlist” option.
- In Tasks/Menu/slack, double-click the “Report Setup Summary” (the first option under “Slack”)

---
Access Timing Reports (2 of 4)
Right click the row

---
Access Timing Reports (3 of 4)
Then select “Report Timing...”

---
Access Timing Reports (4 of 4)
- Then this window opens
- Add “system_clock”
- Select the “Report Timing” button

---
Timing Report Information

---
Worst Negative Slack Summary
- Study the top section: worst negative slack summary
- The top 10 rows show an issue in module FIR_filter_1
- All of them show a problem going from filter_values to filtered_output, we know the addition is the problem:
    - filtered_output_next += filtered_values [ i ];

---
Additions Cause Timing Failure
- There are 16 32-bit integers
- 16 * 32 = 512
- Therefore 512 LUT inputs
- We are asking for too much work to be done in one 200 MHz clock cycle.
- This is why timing fails in the additions
- The solution: more pipelining!
    - We will break up the work of doing the additions into more steps.
    - Then timing should pass.

---
Pipeline The Additions

---
Additional Pipelining:The Additions
/*
** Break up the work of doing the additions so that timing
** constraints will be met.
*/
for ( int i = 0; i!= NUM_ADDERS_STAGE1; i++) // 8
begin
for ( int j =0; j!= NUM_ADDER_INPUTS; j++)
begin
intermediate_add_stage1_next [ i ] = intermediate_add_stage1_next [ i ] + filtered_values [ (i * NUM_ADDER_INPUTS) + j ];
end
end
for ( int i = 0; i!= NUM_ADDERS_STAGE2; i++) // 4
begin
for ( int j =0; j!= NUM_ADDER_INPUTS; j++)
begin
intermediate_add_stage2_next [ i ] = intermediate_add_stage2_next [ i ] + intermediate_add_stage1 [ (i * NUM_ADDER_INPUTS) + j ];
end
end
for ( int i = 0; i!= NUM_ADDERS_STAGE3; i++) // 2
begin
for ( int j =0; j!= NUM_ADDER_INPUTS; j++) // 2
begin
intermediate_add_stage3_next [ i ] = intermediate_add_stage3_next [ i ] + intermediate_add_stage2 [ (i * NUM_ADDER_INPUTS) + j ];
end
end
/*
** Add the final two sums; the final sum is the filter output – the value that will be written to memory
*/
filtered_output_next = intermediate_add_stage3 [ 0 ] + intermediate_add_stage3 [ 1 ];

---
Timing passes!
- Build the project again
- Observe that timing requirements are met due to the absence of timing constraint warnings.

---
 Timing Didn’t Fail In Multiplication
- Why?
- Dedicated DSP blocks were probably used
- Multiplication implemented in hardware
- This is faster
- As such, timing requirements were not violated by the multiplication code

---
Another Pipeline Example
- This is not needed to meet timing requirements in our example project.
- This example is being presented because it’s a common technique used to resolve timing constraint warnings.
- Let’s look at a timer from the SPI code.
  localparam int TIMER_LEN = 16;
  logic [ TIMER_LEN:0 ] end_sclk_to_disable_ss_wait_timer = '0;
  logic [ TIMER_LEN:0 ] end_sclk_to_disable_ss_wait_timer_next = '0;

---
Timer Code Before Pipeline
END_SCLK_TO_DISABLE_SS_WAIT:
begin
end_sclk_to_disable_ss_wait_timer_next =
end_sclk_to_disable_ss_wait_timer – 1'b1;
if ( end_sclk_to_disable_ss_wait_timer == '0 )
begin
SS_n_next = 1'b1;
state_next = SS_DEASSERT_WAIT;
end
end

---
Timer Code After Pipeline
END_SCLK_TO_DISABLE_SS_WAIT:
begin
end_sclk_to_disable_ss_wait_timer_next =
end_sclk_to_disable_ss_wait_timer - 1'b1;
end_sclk_to_disable_ss_wait_timer_elapsed_next =
(end_sclk_to_disable_ss_wait_timer == 1);
if ( end_sclk_to_disable_ss_wait_timer_elapsed == 1'b1 )
begin
SS_n_next = 1'b1;
state_next = SS_DEASSERT_WAIT;
end
end

---
Why Does This Help Timing?
- Because the before code
    - Is doing a 16-bit comparison
    - More work
- The after code
    - Does a 1-bit comparison
    - This means fewer LUT inputs
    - This helps with timing problems
    - As such, this is a common technique to address timing constraint violations

---
Resource Utilization
- You don’t have to be concerned about adding pipeline code from a resource utilization point of view
- Be aware that more pipelining will use more power.
- However, most FPGA applications are not power sensitive

---
Other Timing Failure Types
- This presentation discussed classic logic levels
    - the addition example
    - the comparison example
- The other common timing failure types are:
    - Bad placement - limited resource like a large RAM or DSP multiplier; this is also addressed with pipelining
    - High fanout – many LUTs need to access the same signal; addressed with manual replication of that net within the RTL
    - Fanout of a signal to fixed resources (a special subcase of bad placement) For example, if we need to send a write enable to 4 different RAMs and they are far apart. This problem can be addressed with either pipelining or manual replication of that net within the RTL.

---
Timing Errors Going Forward
- This presentation has been an introduction to the concept
- With complex projects,
    - Correcting timing errors is an ongoing, iterative process
    - Projects are built using multiple builds executed at the same time with the expectation that some will fail and some will pass
    - It’s not uncommon to expect 25% of builds to pass timing requirements
    - It’s not uncommon to run 10 builds simultaneously to get an acceptable build passing timing.