## Slide 1: Pipelining
How To Make Your FPGA Go Faster

## Slide 2: Verilog is NOT Software
always_ff @(posedge clk) Y <= A & B & C;

## Slide 3: Clock Frequency
Fmax determined by longest delay

## Slide 4: Pipelining
Break path into multiple clock cycles
always_ff @(posedge clk) X <= A & B; Y <= X & C;

## Slide 5: Clock Cycle Timing
Data must be aligned within the same clock cycle
always_ff @(posedge clk) X_D1 <= A & B; C_D1 <= C; Y_D2 <= X_D1 & C_D1;

## Slide 6: Multiply-Accumulate

## Slide 7: Counter
always_ff (@posedge clk) if (counter == 8’d49) begin counter <= 8’d0; end else begin counter <= counter + 1; end

## Slide 8: Counter pipelined
always_ff (@posedge clk) begin if (counter_rst) begin counter <= 8’d0; end else begin counter <= counter + 1; end counter_rst <= (counter == 8’d48); end

## Slide 9: Drawbacks
Extra latency
  Usually ok for DSP, networking etc.
  Could cause problems for handshake, like AXI bus.
Extra flops
  Modern FPGA’s has a ton of flops.